## Slide 1: Chapter 2.2

## Slide 2: Addressing
The basic addressing modes are:
Register direct: Moving date to or from a specific register
Register indirect, using a register as a pointer to memory
Program counter-based, using the program counter as a reference point in memory
Absolute, in which the memory addressis contained in the instruction
Immediate, in which the data is contained in the instruction. Some instructions will have an inherent or implicit address (usually a specific register or the memory contents pointed to by a specific register) that is implied by the instruction without explicit declaration.

## Slide 3: Absolute addressing
The most basic form of memory access is absolute addressing, in which the program explicitly names the address that is going to be used. An address is a numeric label for a specific location in memory.
Some hardware instructions or operations rely on fixed absolute addresses. For example, when a processor is first turned on, where does it start? Most processors have a specific address that is used as the address of the first instruction run when the processer is first powered on.

## Slide 4: Data Immediate
In immediate data address mode, the actual data is stored in the instruction.
The sizes allowed for immediate data vary by processor and often by instruction (with some instructions having specific implied sizes).
Many instructions will have inherent or implicit addresses.
These are addresses that are implied by the instruction rather than explicitly stated. The two most common forms of inherent address are either a specific register or a memory location designated by the contents of a specific register.

## Slide 5: Register Direct
In register direct address mode, the source and/or destination is a register.
Many processors distinguish between data and address register operations.
In data register direct operations, flags are typically set or cleared. Data that is smaller than the register may be sign extended or zero filled to fill the entire register, or may be placed only in the portion of the register necessary for the size of the data, leaving the rest of the register unchanged.
In address register direct operations, flags are not normally set or cleared. The address is usually sign extended to the full address size of the processor.

## Slide 6: Register Indirect
In register indirect address mode, the contents of the designated register are used as a pointer to memory. Variations of register indirect include :
Address register indirect with postincrement operations, the designated register is used as a pointer to memory, and then the register is incremented by the size of the operation.
Address register indirect with preincrement operations, the designated register is incremented by the size of the operations, and then the designated register is used as a pointer to memory.
Address register indirect with postdecrement operations, the designated register is used as a pointer to memory, and then the register is decremented by the size of the operation.
Address register indirect with displacement operations, the contents of the designated register are modified by adding or subtracting a displacement integer, then used as a pointer to memory.

## Slide 7: Register Indirect with Index register
In a register indirect with index register mode, two registers are added together to form the effective address of a pointer to memory. These are sometimes called the base register and index register.
In address/base register indirect with index register operations, the contents of the index register are added to the contents of the base address register to form an effective address in memory.
In address/base register indirect with index register and displacement operations, the contents of the index register are added to the contents of the base address register and then an integer displacement is added or subtracted to form an effective address in memory.

## Slide 8: Memory Indirect
In memory indirect address mode, a location in memory contains a value that is used as a pointer (with or without additional effective address computations) to another location in memory.
In memory indirect postindexed operations, the processor calculates an intermediate memory address using a base register and a base displacement.
In memory indirect preindexed operations, the processor calculates an intermediate memory address using a base register, a base displacement, and an index register. The processor accesses the designated memory location, and adds an outer displacement to the memory value to yield the effective address.

## Slide 9: PC relative addressing
PC-relative addressing: the value in the immediate field is interpreted as an offset of the next instruction